## Slide 1: VLSI Final Project: CORDIC Algorithm
Allison Harry

## Slide 2: Introduction
CORDIC algorithm computes trigonometric functions using only add & bitshift operations
  Can also compute square root, exponentials, logarithms
Doesn’t require multiplications or a large lookup table
Hardware efficient when compared with other methods
  Polynomial expansions (Taylor series, etc) require a hardware multiplier
  Lookup tables can get very large, especially for higher accuracy

## Slide 3: CORDIC Algorithm
To compute sin(θ) and cos(θ), successively rotate a unit vector starting at 0 degrees until it points in the direction of angle θ, then y=sin(θ) and x=cos(θ)
After rotation (counter-clockwise),
Choose θ to make multiplication more efficient
  If tan(θ) is a power of 2, then the multiplication becomes a shift
  Choose decreasing θ such that tan(θ) is a multiple of 2
Notes: Image source: https://math.libretexts.org/Bookshelves/Applied_Mathematics/Mathematics_for_Game_Developers_(Burzynski)/04%3A_Matrices/4.04%3A_Rotation_Matrices_in_2-Dimensions

## Slide 4: CORDIC Algorithm
x’ and y’ are scaled by a factor S=cos(1)*cos(2)*…*cos(N)
How to correct the scale factor?
  Correct result with a multiplication – inefficient
  Start with a pre-scaled vector v = (S,0) instead of (1,0) – no additional processing in hardware, just need to precompute S when designing
After N iterations, sin(θ) = y’ and cos(θ) = x’
Notes: Image source: https://math.libretexts.org/Bookshelves/Applied_Mathematics/Mathematics_for_Game_Developers_(Burzynski)/04%3A_Matrices/4.04%3A_Rotation_Matrices_in_2-Dimensions

## Slide 5: Implementations
Iterative
  Computes 1 iteration of the algorithm each clock cycle
  Can only compute one every N cycles
  Low hardware requirement
  Some overhead to keep track of which iteration it’s on
Notes: Image source: https://cnmat.org/~norbert/cordic/node6.html

## Slide 6: Implementations
Loop Unrolled / Pipelined
  Duplicate the iterative hardware N times
  Requires much more area
  Faster, can output 1 result every clock cycle
Compute more than 1 iteration per pipeline stage
  Computation depends on the previous iteration, so computing more than 1 iteration in a clock cycle will increase the critical path

## Slide 7: Implementations
Bit serial
  Execute the additions/subtractions with a bit-serial adder
  Decreases critical path because additions are done 1 bit at a time

## Slide 8: Results
Simulated in Modelsim to ensure designs would output correct results
Synthesis/implementation in Xilinx Vivado for FPGA

## Slide 9: Results
Error decreases with more iterations N
Area can be saved by decreasing N but it will also decrease the accuracy

## Slide 10: Results
Iterative implementation device utilization doesn’t increase much with N
  Will require N clock cycles to compute though
  Good for high accuracy, low speed
Pipelined device utilization increases with N
  Need to add hardware for each new pipeline stage
  Good for high speed, high accuracy

## Slide 11: Conclusion
Iterative implementation – low throughput, low area, constant with N
Pipelined implementation – high throughput, high area, more costly with N
Bit serial implementation
  Faster critical path doesn’t compensate for using more clock cycles to compute the additions one bit at a time
  Requires additional control logic
  Widely used, so could probably be optimized to be competitive with the other implementations